## Slide 1
Summary: Automating predictable, reproducible Synthetic Cell generation.
1
Vesicle manufacturing must be possible on-site, on-demand, with a suitable monodispersity in vesicle size, and characterized in minutes. This common task remains challenging for researchers. Solution: build a low-cost, integrated system with computational metrology for non-expert vesicle production.
Deliverables:
WP1: Standardized device for Synthetic Cell production. Formation of a microfluidic device for the reproducible production of cell-sized (10-50 micron) production of lipid vesicle based synthetic cells. Democratized Techniques. A <$10k end-to-end microfluidic chip fabrication system which can reproducibly manufacture devices without expert users.
WP2: Automation Tools. An affordable vision based microfluidic controller for automation of synthetic cell production. Automation achieved using cheap Raspberry Pi compatible controller.
WP3: Biological Integration. Demonstration of robust integration of PURE protein expression systems into microfluidic Giant Lipid vesicles.

## Slide 2
2
Vesicle manufacturing must be possible on-site, on-demand, with a suitable monodispersity in vesicle size, and characterized in minutes. This common task remains challenging for researchers. Solution: build a low-cost, integrated system with computational metrology for non-expert vesicle production.
Timeline:
WP2: Automation Tools.
WP1: Standardized device for Synthetic Cell production.
Summary: Automating predictable, reproducible Synthetic Cell generation.
September, ‘25
September, ‘25
January, ‘25
May, ‘25
September, ‘24
Finalised Device
Device dev
Code dev on PDMS devices
Test on WP1 Device
Test PURE SynCell production on WP1
Test on PURE SynCell device

## Slide 3
WP1: Development of standardized microfluidic device
3
m.fletcher@imperial.ac.uk
Aim: Standardized manufacture of a device to produce Giant unilamellar Lipid Vesicles (GUVs) as the essential chassis of Synthetic Cells.
  Extensions: Low-cost manufacture < $10k from CAD to chip. Device ideally made from glass.
  Fall back: Seek commercial manufacture.
Minimum deliverable: Produce stable monodisperse GUVs with previously optimized conditions using novel device made in this project
Expected deliverable: Produce stable, monodisperse GUVs encapsulating PURE cell-free protein systems and demonstrate highly uniform GFP production rates.

## Slide 4
Synthetic Cell microfluidic Device requirements
Dimensions:
  Produce Cell-sized Lipid Vesicles – (10-50 microns)
  Minimum channel dimension needs to be around 20-40 microns.
  Footprint – Ideally fit standard microscopy slide footprint (25mm x 75mm)
4
m.fletcher@imperial.ac.uk
Fluidic Interfaces
  At least 3 fluidic inlets (‘Cytoplasm’, ‘Lipids’, Outer Aqueous medium).
  1 outlet for SynCell collection.
  Interface common fluidic connections e.g. Luer lock, or 750 micron steel couplers common. (May be an issue for hard materials).
  Material Property requirements
    Optically transparent
    Can manufacture hydrophobic and hydrophilic channel surface selectively (**Critical** for double emulsion droplet microfluidics
    Anti-fouling surfaces ( low-binding of biomolecules).

## Slide 5
WP2: Automation of Synthetic Cell production
Minimum deliverable:
Monodisperse size. Demonstrate GUV production using OLA with a normalized standard deviation in sizes of < 10%.
Deskilled operation. Automatic Controller should demonstrate the production of GUVs without human intervention from the point of correct fluidic connection of all input fluids.
5
m.fletcher@imperial.ac.uk
  Aim: Demonstrate computer controlled operation of microfluidic giant vesicle production.
Expected deliverable:
Same as minimum deliverable, but controller footprint is minimized by compatibility with Raspberry Pi

## Slide 6
  Flow Control
    Computer controlled flow control using accessible flow control systems.
    Either Custom made Low-cost syringe pumps or Commercial Pumps e.g. Elveflow/Fluigent pressure controllers
Automation of Synthetic Cell production: Requirements
  Ease of code sharing
    Release code for controller on GitHub.
    Preferably write in Python to allow easy extension by third party
    Modularise to allow extension to different microfluidic control tasks.
  Computer vision based feedback
    Vision based feedback enables wide applicability of controller for producing Synthetic Cells for different experiments.
    For initial demonstration, using dark field fluorescence will likely greatly reduce complexity of object detection task.

## Slide 7
WP3: Robust integration of PURE expression systems.
  Aim: Producible stable GUVs in large population sizes (100s per experimental run) which produce GFP using microfluidic device.
  Minimum Deliverable: Demonstration of GFP production using GUVs in sample sizes > 100 GUVs using microfluidic devices using previously published protocols.
  Expected Deliverable: Demonstration of GFP production within >100 Synthetic Cells (10s uM final concentration) using standardized device from WP1.